## Slide 1: Meeting Water Planning Goals with New Data on Urban Conservation Programs
Katie Anderson, CEO

## Slide 2
WORLD TOILET DAY
November 19, 2015

## Slide 4: Project Overview
Low-hanging fruit: conservation without behavior change or capital-intensive infrastructure
Targeting high-density real estate
  100 unit apartment complex is the same as 100 single-family homes but with just one driveway
Projecting savings with data
  Comprehensive audit of historical water consumption
  Monitor occupancy and tenant density

## Slide 5: Project Overview
Baseline program: showerheads, aerators, manifolds, drips/leaks, rebuild toilets
Benchmarked to 55 gpcd
Crew member can complete 7 units per day
Baseline program plus toilet replacement: everything in baseline plus replace current toilets
Benchmarked to 40 gpcd
Crew member can complete 2 units per day

## Slide 6: Case Study: Baseline
260 units/10 days
Water Savings
984,000 gallons/
3.02 acre-feet per month
11,808,000 gallons/
36.24 acre-feet per year

## Slide 7: Case Study: Baseline
348 units/15 days
Water Savings
3,128,300 gallons
9.60 acre-feet per month
37,539,600 gallons
115.21 acre-feet per year

## Slide 8: Case Study: Baseline plus Toilets
154 units/7 days
Water Savings
641,000 gallons/
1.97 acre-feet per month
7,690,000 gallons/
23.60 acre-feet per year

## Slide 9: Project Impact
Chart: Residential Units
| 216 | 255 | 299 | 156 | 260 | 260 | 168
Before Save Water Co | 2230000 | 2490000 | 1639529 | 1410489 | 2400000 | 2300000 | 1089000
With Save Water Co | 1200000 | 1270000 | 1064300 | 859600 | 1423000 | 1570000 | 730000
Water Savings | 0.46188 | 0.48996 | 0.35085 | 0.39057 | 0.40708 | 0.31739 | 0.32966

## Slide 10: Just One Leak

## Slide 11: Toilet Truth
Chart: 
| Toilet Leak | Toilet Inefficient | Diverter Leak | Shower Leak | Sink Leak
Percent | 0.08 | 0.67 | 0.43 | 0.13 | 0.08
Region L 2015 IPP Assumptions:
Toilet retrofit 25 yr lifespan, showerhead/aerator 15 yrs
Out of 6400 units

## Slide 12: Toilet Truth
Chart: 
| 1.28 gpf | 1.6 gpf | 1.6 gpf dual-flush | 3.5 gpf
Labeled | 1.28 | 1.6 | 1.6 | 3.5
Measured | 1.9 | 2.5 | 2 | 3.9
Lower labeled use does not necessarily guarantee consistency or durability
(up to 2.34)
(up to 4.08)
(up to 2.22)
(up to 4.84)

## Slide 13: Regional Impact
Potential new water with full implementation of such conservation programs:
  Region C: 81,000 acre-feet
  Region H: 75,000 acre-feet
  Region K: 21,000 acre-feet
  Region L: 23,000 acre-feet

## Slide 14: Project Cost
$1,100 per acre-foot Save Water Co baseline program
  1 acre-foot per approx. 9.5 units
  Approx. $120 per unit
$2,607 per acre-foot baseline plus toilet replacement
  1 acre-foot per approx. 6.6 units
  Approx. $395 per unit
$250 per acre-foot after initial implementation

## Slide 15: Cost Comparison
2012 SWP: $6,000 per acre-foot for all new sources ($53 Billion total)

## Slide 16: Project Benefits
Real-world monitoring and data
Does not depend on behavior change
Eases urban – rural competition
Enlists “unengaged middle”

## Slide 17: Contact Info
Katie Anderson
kanderson@savewaterco.com
@SaveWaterCo